Meeus chapter 24 page 151
T = { JD - 2451545.0} over 36525

L_o = 280^o .46645 + 36 000^o .76983T + 0^o .000 3032T^2

M = 357^o .52910 + 35 999^o .05030T - 0^o .000 1559T^2 - 0^o .000 000 48T^3

e = 0.016 708 617 - 0.000 042 037T - 0.000 000 1236 T^2

C = ( 1^o .914 600 - 0^o .004 817T - 0^o .000 014T^2) sin M + ( 0^o .019 993 - 0^0 .000 101 T ) sin 2M + 0^o .000 290 sin 3M

Sun true geometric longitude, mean equinox of date, Θ = L0 + C. True anomaly %nu = M + C

That is the equation of the centre – might be better to use chapter 29 page 195 tan %nu = { sin L_0 } over { cos L_0 - e }
So %THETA = %nu + L_0 - M

For apparent longitude λ referred to true equinox of date, need nutation and aberration.

%OMEGA = 125^o .04 - 1934^o .136 T

%lambda = %THETA - 0^o .00569 - 0^o .00478 sin %OMEGA (includes aberration 20”.49552 and nutation)

Chapter 21 page 135 – mean obliquity of the ecliptic -

ε = 23° 26’ 21”.448 – 46”.8150 T – 0”.000 59 T2 + 0”.001 813 T3

Sun RA and DEC, add 0^o .00256 cos %OMEGA to ε (seems to be 1st nutation term), then –

tan %alpha = { cos %epsilon sin %lambda } over {cos %lambda} , sin %delta = sin %epsilon sin %lambda

Chapter 11 page 83 – mean sidereal time at Greenwich at 0h UT is –

%theta _0 = 6^h 41^m 50^s .54841 + 8640 184^s .812 866 T + 0^s .093104 T^2 - 0^s .000 0062 T^3

or, in degrees –

%theta _0 = 100.460 618 37 + 36 000.770 053 608 T + 0.000 387 933 T^2 - T^3 / 38 710 000

or, for any instant (not just 0h UT) –

%theta _0 = 280.460 618 37 + 360.985 647 366 29 ( JD - 2451545.0 ) + 0.000 387 933 T^2 - T^3 / 38 710 000

Correction for equation of the equinoxes –

{ %DELTA %psi cos %epsilon } over 15 where (chapter 21 page 132) Δψ = -17”.20 sin Ω

Chapter 14 page 98 – rising and setting

cos H_0 = { -sin(0^o .8333) - sin %phi sin %delta } over { cos %phi cos %delta }

Transferring time scales
T = { JD - 2451545.0 } over 36525
%tau = ( JD - 2440587.5 ) times 86400 - %DELTA T where %DELTA T = 45 + 50 times{{ JD - 2440587.5 } over 36525}
%tau = ( JD - 2440587.5 ) times left ( 86400 - 50 over 36525 right ) - 45
36525 times (T + 0.3) = JD - 2440587.5
%tau = 36525 times ( T + 0.3 ) times left( 86400 - 50 over 36525 right) - 45 = ( ( T + 0.3 ) times 3155759950 ) - 45 = 946727940 + 3155759950 T
T = { %tau + 45 } over { 3155759950 } - 0.3 = { %tau - 946727940 } over { 3155759950 }
e.g. JD = 2452000.0, T = 0.01245722108145106091, τ = 986039939.37714
When τ = 0, T = -0.29999998574036025775
L_0 = { %tau ^2 } over 1.881920840487384e+24 + %tau over 5022440.577213014 + 4.891041609478770
M = { - %tau ^2 } over 3.639856059152292e+24 + %tau over 5022680.440480501 + 6.245041296911722
e = -1.241110787093734e-26 %tau ^2 - 1.329722180026880e-14 %tau + 0.01672121697540164
Using 2 terms, e = -1.336772145802711e-14 %tau ^2 + 0.01672128001139845
L_0 - M = { %tau ^2 } over 1.240528398723951e+24 + %tau over 105168725144.5198 + 4.929185619746672

After some fitting, I get
L_0 = %tau over 5022440.501755778 + 4.890899777335416
M = %tau over 5022680.079203663 + 6.244922869391880
%lambda = L + 0.03336588305199348 sin (M) + 0.0003479109925478395 sin (2M)
Max error in λ is less than 0.011 degree.

Nutation – top terms (arcseconds)
%DELTA %psi = (-17.1996 - 0.01742T) sin (%OMEGA) + ( -1.3187 - 0.00016T ) sin ( 2F - 2D + 2%OMEGA )
%DELTA %epsilon = ( 9.2025 + 0.00089T ) cos ( %OMEGA ) + ( 0.5736 - 0.00031T ) cos ( 2F - 2D + 2%OMEGA )
Gonna use just the first term!
Ω = 125° 02’ 40”.280 – (5r + 134° 08’ 10”.539)T + 7”.455T2 + 0”.008T3
%OMEGA approx 6.026350588021488 - %tau over 93484602.19177055
T = (JD - 2451545.0) over 36525 (in the TDB timescale)

%epsilon approx {-%tau} over 1.390477787189644e13 + 0.409160888937511

Putting it all together (needs to be checked and tested!)
#include <math.h>

void getSunRaDec(double sec, double *ra, double *dec) {
  double l = mod(sec/5022440.501755778+4.890800412250441,2*M_PI);
  // ^^ Includes aberration
  double m = mod(sec/5022680.079203663+6.244922869391880,2*M_PI);
  double o = mod(6.026350588021488-sec/93484602.19177055,2*M_PI);
  double e = 0.409160888937511-sec/1.390477787189644e13+0.0000446188*cos(o);
  double dp = -8.34620e-5*sin(o);
  double lam = l + 0.03336588305199348*sin(m) + 0.0003479109925478395*sin(2*m);
  *ra=atan2(cos(e)*sin(lam),cos(lam));
  *dec=asin(sin(e)*sin(lam));
}